## Slide 1
how to control vehicle using a joystick
Department of Mechanical and Aerospace Engineering
EML 4930 – Joystick interface

## Slide 2: ROS2 package ‘joy’
ROS2 comes with a package named ‘joy’.
The package has two executables
  joy_node
    publishes a topic named ‘joy’
    message type is sensor_msgs/Joy
      std_msgs/Header header
      float32[] axes
      int32[] buttons
      axes are float values between -1 and +1
      buttons are integer values, 0 or 1
  enumerate_devices
    node gives identify of joystick(s)

## Slide 3: vehicle interface
you will log into the vehicle computer and run a launch file named vehicle.launch.py
this will start 2 nodes (launch file is vehicle.launch.py
node 1 – talks with Arduino computer
  package: motor_carrier_driver
  executable: driver
  subscribes to:
  publishes:
node 2 – talks with GPS sensor and speed/steering control
  package: neo6m_driver
  executable: driver
  subscribes to:
  publishes:
Notes: Ackerman
steering -45 to +45 in radians
speed -2.5 to+2.5 ; max speed 6.0

## Slide 4: node 1: motor_carrier_driver
subscribes to:
  msg_type=Joy, topic="joy", callback=self.joy_callback, qos_profile=1
  msg_type=AckermannDriveStamped, topic="vehicle_command_ackermann“, callback=self.ackermann_callback, qos_profile=1
publishes:
  msg_type=Odometry, topic="odometry", qos_profile=1

## Slide 5: node 2: neo6m_driver
subscribes to:
publishes:
  msg_type=NavSatFix, topic="gps", qos_profile=10

## Slide 6
map_joy_to_ack
map_joy_to_ack.py
‘map_joy’
P
S
Ackermann_msgs/AckermannDriveStamped
std_msgs/Header header
ackermann_msgs/AckermannDrive drive
topic name: vehicle_command_ackermann
P
nav_msgs/Odometry
geometry_msgs/PoseWithCovariance pose
geometry_msgs/TwistWithCovariance twist
topic name: my_polar_topic
published every time ‘joy’ comes in
published at 20 Hz
motor_carrier_driver
motor_carrier_serial_driver.py
‘driver’
pkg: <your joystick package>
node name
python file name
executable name
sensor_msgs/Joy
std_msgs/Header header
float32[] axes
int32[] buttons
topic name: joy
P
neo6m_driver
neo6m_driver_node.py
‘driver’
sensor_msgs/NavSatFix
double latitude
double longitude
double altitude …
topic name: gps

## Slide 7
map_joy_to_ack
map_joy_to_ack.py
‘map_joy’
P
S
P
motor_carrier_driver
motor_carrier_serial_driver.py
‘driver’
node name
python file name
executable name
P
neo6m_driver
neo6m_driver_node.py
‘driver’