## Slide 1
PID control
Department of Mechanical and Aerospace Engineering
EML 4930 – wall following

## Slide 2: Objective
Travel in the hallway, maintaining a distance of 1 meter from the right-side wall.
Get d1 and (x1,y1) for lidar beam along –ysensor
Get d2 and (x2,y2) for lidar beam at angle θ from the first beam
Calculate d3
xsensor
ysensor
(x1, y1)
(x2, y2)
d1
d2
θ
d3

## Slide 3: Objective
Travel in the hallway, maintaining a distance of 1 meter from the right-side wall.
xsensor
ysensor
(x1, y1)
(x2, y2)
d1

d2
dwall
θ

let v be a unit direction vector pointing from P1 to P2
dwall = d1 cos 

## Slide 4: Objective
Travel in the hallway, maintaining a distance of 1 meter from the right-side wall.
xsensor
ysensor
dwall
error = dwall – 1 (units of meters)
if error > 0, turn right
if error < 0, turn left

## Slide 5: PID control
e = = dwall – 1 (units of meters)
let u represent the control input (steering angle)
the control effort at time t depends on the current error, the current rate of change of the error and the summation of all past errors
in a discreet time implementation
subtract the prior control effort from the current control effort
xsensor
ysensor
dwall

## Slide 6: PID control
e = = dwall – 1 (units of meters)
u must be bounded between -45 and +45 degrees
xsensor
ysensor
dwall

## Slide 7: PID tuning
synthesize the gains
start with Kd = Ki = 0
increase Kp until there is considerable overshoot and or instability
back off Kp
  add Kd to reduce overshoot
  add Ki to reduce steady state error